## Slide 1: ST built-in Boot Loader By Omer Korech
Applicable to: STM32L1XX
Due to the technical limitations that will be detailed below, my company has decided not to use ST built in boot loader therefore this presentation is released for the public in hope not to repeat our mistakes 

## Slide 2: Added value in brief
Undocumented important Takeaways:
  When running from bank 2 (nBFB2 = 0), an attempt to update firmware from system memory will FAIL, because it will result in jumping back to bank 2
  Unlike STM32L0XXX and STM32L4XXX, nBFB2 does not result in bank swap
  A concrete bootloader flowchart is presented in slide #7

## Slide 3: Basic Computer System
A processor is a device that executes instructions
  Processor has some internal state in storage elements (registers)
A memory holds instructions and data
  von Neumann architecture is assumed for simplicity
A bus connects the two
regs
bus
processor
memory
01010000
10010100
…
addr, data,
r/w

## Slide 4: ARM Cortex-M Start UP Sequence
Electronically
  Fetch Stack Pointer from address 0x00
  Fetch Program Counter from address 0x04
Software
  Execute assembly function Reset_Handler Initialize vector table and call the followings:
  Execute c function SystemInit Initializes clocks and VTOR
  Execute assembly function __iar_data_init3Initialize Initializes variables
  Call function main User program
  But address 0x00 does not exist in Flash ! It is mapped to other address (0x08000000 in normal execution)

## Slide 5: System Memory
Written in ROM within the Flash
Has two functions:
  Firmware update (When nBFB2 = 1)
  Execute code from bank 2 (When nBFB2 = 0)

## Slide 6: nBFB2 bit
nBFB2 = 1 at startup
  Normal Execution
nBFB2 = 0 at startup
  Address 0x00 is mapped electronically to System memory
  System memory Jumps to bank 2
Undocumented important Takeaways:
  When running from bank 2 (nBFB2 = 0), an attempt to update firmware from system memory will FAIL, because it will result in jumping back to bank 2
  Unlike STM32L0XXX and STM32L4XXX, nBFB2 does not result in bank swap

## Slide 8: BL.C
#include "BL.h"
void GoToBootLoader(void)
{
//Initializing the arguments for HAL functions
FLASH_AdvOBProgramInitTypeDef OBbank1;
OBbank1.BootConfig = OB_BOOT_BANK1;
OBbank1.OptionType = OPTIONBYTE_BOOTCONFIG;
// Write to EEPROM that BootLoader should be executed
HAL_FLASHEx_DATAEEPROM_Unlock();
HAL_FLASHEx_DATAEEPROM_Program(FLASH_TYPEPROGRAMDATA_WORD,
EEPROM_Address_Mode_Of_Execution,
ShouldExecuteBootLoader);
//Change to (or stay at) bank1 and reset the device
HAL_FLASH_OB_Unlock();
HAL_FLASHEx_AdvOBProgram(&OBbank1);
HAL_FLASH_Unlock();
HAL_FLASH_OB_Launch();
}

## Slide 9: void SystemInit (void)
// Define our function pointer
void (__code*SysMemBootJump)(void);
// Set system memory address.
volatile uint32_t addr = BootLoaderMemoryLocation;
if(…) // MCU was Set to be boot from bank 1
if ( // Jump to boot loader request is registered
// Reset our trigger
HAL_FLASHEx_DATAEEPROM_Erase(FLASH_TYPEPROGRAM_WORD, EEPROM_Address_Mode_Of_Execution);
//Set jump memory location for system memory
SysMemBootJump = (void (*)(void)) (*((uint32_t *)(addr + 4 )));
//Remap system memory to address 0x0000 0000 in address space
__HAL_SYSCFG_REMAPMEMORY_SYSTEMFLASH();
SCB->VTOR = 0; // BootLoaderMemoryLocation; Since 0 is mapped to system memory
__set_MSP(*(uint32_t *)addr);
// Point the PC to the System Memory reset vector
SysMemBootJump();
}
else{ // Running Code from bank 1
SCB->VTOR = FLASH_BASE | VECT_TAB_OFFSET; /* Vector Table Relocation in Internal FLASH.*/
}
}
else // run from bank2
{
SCB->VTOR = FLASH_BANK2_BASE | VECT_TAB_OFFSET;
}

## Slide 10: Requirement from external application
Input
The input to the external (smarthphone) is a binary file of size X bytes, where in our case 0x38000 < X < 0x40000 changes from one update to the other.
Goal
The binary file is to be copied into flash, where the first byte is copied to address UpdateCodeStartAddress and the last address is to be copied to UpdateCodeStartAddress + X, where UpdateCodeStartAddress = 0x08008000.
After the file is copied (and verified that it is copied correctly), the micro-controller should be booted from bank 2.

## Slide 11: Bootloader limitations
ST bootloader has limited address range allowed to be written (all of bank 1 and ½ of bank 2).
Usually two valid applications should be available, in order to accommodate a failure during update of one of the versions.
If the application requires more than ½ the space of a bank, only one out of the two application may be updated 
Why?
Hint: The firmware update by ST built in bootloader may only take place when nBFB2 = 1.
Due to the above limitation, it has been decided to use custom boot loader, and therefore this presentation is brought back to the public domain (as my knowledge in this field comes from the public domain)

## Slide 12: Memory banks in STM32L1XX
Two Banks
All of Bank 1 and Half of Bank 2 are accessible by ST ROM Bootloader
Factory Code @ Bank1 (start address 0x08000000) | Updated Code @ Bank2 (start address 0x08040000)
Updated Graphics data @ bank 1 (start address 0x08008000) | Factory Graphics data @ bank2 (start address 0x08048000)